## Slide 1: Smart Irrigation System using IoT
FINAL YEAR PROJECT · B.TECH ELECTRONICS & COMMUNICATION
PRESENTED BY
Aarav Sharma · Diya Patel
GUIDED BY
Prof. R. K. Mehta
DEPARTMENT
Electronics & Communication, 2025–26
Soil-moisture driven watering for small farms

## Slide 2: Agenda
01
Introduction
02
Literature & Gap
03
Proposed System
04
Implementation
05
Results
06
Conclusion

## Slide 3: Introduction
01

## Slide 4
KEY IDEA
Up to half of irrigation water on small farms is lost to over-watering.
Why this project matters

## Slide 5: Introduction
CONTEXT
Flood irrigation is still the most common method on small Indian farms.
Agriculture depends heavily on timely, measured irrigation
Manual watering wastes water, power and labour
Low-cost sensors and microcontrollers make automation affordable
This project builds a sensor-driven pump controller with a phone dashboard

## Slide 6: Problem statement
1
Over-watering
Fields are watered on a fixed schedule, not on actual soil need.
2
No visibility
Farmers cannot see soil conditions without visiting the field.
3
High cost
Commercial drip automation is too expensive for small plots.

## Slide 7: Literature & Gap
02

## Slide 8: Literature survey
Study | Approach | Limitation
Kumar et al. | GSM-based pump control | No sensor feedback
Rao & Singh | Timer-based drip system | Ignores weather and soil
Fernandes | Cloud dashboard prototype | Needs constant Wi-Fi
Representative summaries — replace with your own citations.

## Slide 9: Proposed System
03

## Slide 10: System architecture
01
Sense
Moisture, DHT11 and rain sensors read field data
02
Process
ESP32 compares readings with crop thresholds
03
Act
Relay switches the pump on or off
04
Notify
Readings and alerts sync to the app

## Slide 11: Block diagram
Block diagram / flowchart
Every module talks through one simple, testable interface.
Sensors feed an ESP32 controller. A relay module drives the pump, and readings are pushed every minute to a lightweight cloud database that the mobile dashboard reads.

## Slide 12: Technology stack
1
ESP32
Wi-Fi microcontroller running the control loop
2
Sensors
Capacitive soil moisture, DHT11, rain sensor
3
Firebase
Real-time database for readings
4
Flutter
Cross-platform mobile dashboard

## Slide 13: Implementation
04

## Slide 14: Project timeline
Jul
Requirement study
Survey of users and existing tools
Aug
Design
Architecture, database and UI wireframes
Sep–Oct
Development
Modules built and unit tested
Nov
Testing
Integration and field testing
Dec
Report
Documentation and final review

## Slide 15: Results
Chart: 
| Week 1 | Week 2 | Week 3 | Week 4
Water used (litres) | 820 | 640 | 560 | 530
35%
less water than the manual baseline
Automatic switching cut water use steadily as thresholds were tuned for the crop.
Sample data for illustration — replace with your own figures.

## Slide 16: Conclusion
A low-cost controller can automate irrigation reliably
Sensor feedback avoids over-watering and saves power
The dashboard gives farmers visibility without field visits

## Slide 17: Thank you
Aarav Sharma · Diya Patel
Dept. of Electronics & Communication
Questions and suggestions are welcome.